| Posted: Tue Mar 08, 2005 10:32 am Post subject: Cell Phone Mute Function on Stock 2005 Radio xB/xA/tC |  |
| --- | --- |
| I put a new Motorola Bluetooth hands free kit for my cell phone in my XB and wanted to mute the radio when the phone was in use and or when it rang. All hands free kits wired and wireless have a wire to mute a radio if supported. My stock pioneer radio did not have this function documented, well I took the radio apart and found that the un-used pin on the smaller connector was the mute function. I was not able to find a proper metal socket/pin to put into the connector so I took a #14 wire stripped off about 1/4 inch folded it back against itself to make a 1/8" doubled up end and forced it into the blank hole to make contact with the radio's pin then zip tied it to the wire next so it would not work it's way out. I then connected the end of this wire to the mute wire from the cell phone hands free kit and it works great. My radio is the single CD stock pioneer that is used in the 2005 XB XA & TC. I do not know if this works in the 6 cd version but if it has the same missing wire in the smaller connector it probably would. To test just ground that pin on the radio's connector if the radio mutes then comes back when removed you have it. This is not documented by Toyota and I am not responsible if it kills your radio but it worked for me. I have been using it for about a month now, I use my XB for work and am on the phone on and off all day long. _________________ Doug Laing doug@laingelectronics.com MSM/Trillian IM doug-laing@hotmail.com |